CRANK INSTRUCTIONS

Ref:- L35 = Brass

Parts in the kit include 1 x crank base, 1 x crank arm, 1 x 8 BA washer, 1 x piece of 1mm wire.  Examine parts to ensure they are correctly cast; sometimes cast parts may become slightly bent in the lost wax process.  Using hard nose cutters or junior hack saw, remove remains of spru from base and arm.  The main centre hole of the crank arm has already been reamed 1/8”, but the base will require gentle needle filing to remove any flash, moulding joint lines then sufficient metal to give a nice fit, without binding.  The thickness of the arm may also need adjustment to allow the washer and then the pin to be fitted.  The crank base has already been drilled No. 60, to take the 1 mm diameter wire.  Ensure the 1/16” Rodding holes in the arms are clear; you may need to re-drill this hole to suit your diameter rodding.  Assembly - apply a small amount of copper grease to the bearing surfaces and install the arm onto the base, followed by the washer then the pin.  The pin can be crimped and cut to length, which should be sufficient to hold the parts, but will allow disassembly should it be required.  The base can be fixed in position by drilling a 3 mm hole and pushed into place, alternatively on some surfaces such as concrete; drill an oversize hole, fill with epoxy glue and insert base and allow to harden.  Remember in service to apply more lubrication each year.